## Slide 1: Raspberry Setup
LOREM IPSUM DOLOR

## Slide 2: Rabian - Basic
OS
  Download Rasbian system image
    https://www.raspberrypi.org/downloads/raspbian/
    Windows
      Remove all partitions
      Download Win32DiskImager
      Write Rasbian image to TF card
    Linux
      Etcher
      dd bs=4M if=2018-11-13-raspbian-stretch.img of=/dev/sdX conv=fsync
Config
  SSH
    Create empty “ssh” file in /boot to enable SSH service
Boot
  Username: pi
  Password: raspberry
SSH
  IP address can be found using Angry IP Scanner
  ssh pi@raspberrypi.local
  rsync -avz -e ssh pi@192.168.1.10:camera/ camera/

## Slide 3: Rasbian - Hardware Support
LCD
  Modify config.txt
WIFI
  /etc/wpa_supplicant/wpa_supplicant.conf
  Static IP
    /etc/dhcpcd.conf
USB Camera
  IMX179
    FOV: 145
    max: 3264x2448, 30fps
  OV2710
    FOV: 145
    max: 1920x1080, 29fps
  OV5648
    max: 2592x1944, 30fps
    FOV: 70
    auto focus
  /dev/video0
  fswebcam <filename>
    -r <resolution>
    --fps <framerate>
  v4l2-ctl -V
config.txt
max_usb_current=1
hdmi_group=2
hdmi_mode=87
hdmi_cvt 800 480 60 6 0 0 0
wpa_supplicant.conf
country=CN
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
network={
scan_ssid=1
ssid="yushidata"
psk="yushi@408"
key_mgmt=WPA-PSK
}
dhcpcd.conf
interface wlan0
static ip_address = 192.168.1.99
static routers = 192.168.1.1

## Slide 4: Camera
sudo cat /sys/kernel/debug/usb/devices
v4l2-ctl
  v4l2-ctl --list-devices
    List devices
  v4l2-ctl --list-formats-ext
  v4l2-ctl -d /dev/video0 --list-formats
    list formats of video0
  v4l2-ctl -d /dev/video0 -l
    List controls
  v4l2-ctl -d /dev/video0 -D
    Show driver info
  v4l2-ctl -d /dev/video0 --all
    Show all info

## Slide 5: Rasbian - Config
Apt source
  sudo nono /etc/apt/sources.list
  sudo nono /etc/apt/sources.list.d/raspi.list
Update S/W
  sudo apt update
  sudo apt upgrade
  sudo rpi-update
  sudo apt install vim
Auto login
  sudo raspi-config
  “3 Boot Options” -> “B1 Desktop/CLI” -> “B2 Console Autologin”
  “Localization Options” -> “Change TimeZone” -> “ShangHai”
Lauch python scripts when startup
  sudo crontab -e
  Add “@reboot sh /home/pi/bbt/launcher.sh >/home/pi/logs/cronlog 2>&1”
sources.list
deb http://mirrors.aliyun.com/raspbian/raspbian/ stretch main contrib non-free rpi
raspi.list
deb http://mirrors.aliyun.com/debian/ stretch main ui

## Slide 6: Auto Start Program
Add script file to /etc/init.d/
  chmod 755
  test
    sudo /etc/init.d/yushi.sh start/stop
  enable when startup
    sudo update-rc.d yushi.sh defaults
  disable from startup
    sudo update-rc.d -f yushi.sh remove
#! /bin/sh
case "$1" in
start)
echo "noip is starting"
# Starting Programm
/usr/local/bin/noip2
;;
stop)
echo "noip is ending"
# Ending Programm
killall noip2
;;
*)
echo "Use: /etc/init.d/noip {start|stop}"
exit 1
;;
esac
exit 0

## Slide 7: Install Python Env
Pip/Virtualenv/Virtualenvwrapper
  sudo apt install python3-pip
  sudo pip3 install virtualenv virtualenvwrapper
  sudo apt install virtualenv virtualenvwrapper
  sudo rm -rf ~/.cache/pip
  Append lines to ~/.profile
  source ~/.profile
  mkvirtualenv py3 -p /usr/bin/python3
~/.profile
# virtualenv and virtualenvwrapper
export WORKON_HOME=$HOME/.virtualenvs
export VIRTUALENVWRAPPER_PYTHON=/usr/bin/python3
source /usr/share/virtualenvwrapper/virtualenvwrapper.sh

## Slide 8: Install Miniconda3
Miniconda3
  wget http://repo.continuum.io/miniconda/Miniconda3-latest-Linux-armv7l.sh
  md5sum Miniconda3-latest-Linux-armv7l.sh
  bash Miniconda3-latest-Linux-armv7l.sh
  source ~/.bashrc
  python --version (...Continuum...)
Virtualenv
  conda create --name py2 python=2
  source activate py2
  source deactivate
  conda install anaconda-client
Opencv
  conda install --channel https://conda.anaconda.org/poppy-project opencv3

## Slide 9: Berryconda
Berryconda
  wget https://github.com/jjhelmus/berryconda/releases/download/v2.0.0/Berryconda3-2.0.0-Linux-armv7l.sh
  bash Berryconda3-2.0.0-Linux-armv7l.sh
  source ~/.bashrc
  python --version (...Continuum...)
Virtualenv
  conda create --name py3 python=3
  source activate py3
  source deactivate
  conda install anaconda-client
Opencv
  conda install opencv3 scikit-learn

## Slide 10: Install OpenCV
Install numpy and dependencies
  pip install numpy
Download and build opencv
  sudo apt install python3-dev
  sudo apt install build-essential cmake pkg-config libjpeg-dev libtiff5-dev libjasper-dev libpng12-dev libavcodec-dev libavformat-dev libswscale-dev libv4l-dev libxvidcore-dev libx264-dev libatlas-base-dev gfortran
  wget -o opencv.zip https://github.com/opencv/opencv/archive/3.4.3.zip
  wget -o opencv_contrib.zip https://github.com/opencv/opencv_contrib/archive/3.4.3.zip
  unzip opencv.zip
  unzip opencv_contrib.zip
  cd opencv-3.4.3 && mkdir build && cd build
  cmake -D CMAKE_BUILD_TYPE=RELEASE -DCMAKE_INSTALL_PREFIX=/usr/local -D OPENCV_EXTRA_MODULES_PATH=~/opencv_contrib-3.4.3/modules -D ENABLE_NEON=ON -D ENABLE_VFPV3=ON -D BUILD_TESTS=OFF -D INSTALL_PYTHON_EXAMPLES=OFF -D BUILD_EXAMPLES=OFF
  Modify /etc/dphys-swapfile
    CONF_SWAPSIZE=1024
  sudo /etc/init.d/dphys-swapfile stop && sudo /etc/init.d/dphys-swapfile start
  make -j4 && sudo make install && sudo ldconfig
  cd /usr/local/lib/python3.5/site-packages && sudo mv cv2.cpython-35m-arm-linux-gnueabihf.so cv2.so
  cd ~/.virtualenvs/py3/lib/python3.5/site-packages/ && ln -s /usr/local/lib/python3.5/site-packages/cv2.so cv2.so
  Revert /etc/dphys-swapfile
    CONF_SWAPSIZE=100
  sudo /etc/init.d/dphys-swapfile stop && sudo /etc/init.d/dphys-swapfile start

## Slide 11: Clone SD Card
Backup
  sudo fdisk -l
  sudo dd bs=4M if=/dev/sdb of=~/hw/raspbian_11292018.img
    16G 13min
  sudo umount /dev/sdb1 /dev/sdb2
  fdisk -l raspbian.img
Restore or Clone
  Remove partitions if any
    sudo gparted
  sudo dd bs=4M if=~/hw/raspbian_11292018.img of=/dev/sdb
    5.0G 10min
    8.0G 20min

## Slide 12: V4L (Video4Linux) and Pillow
Commands
  v4l2-ctl
    v4l2-ctl --list-devices
    v4l2-ctl --list-formats-ext
    v4l2-ctl -d /dev/video0 --list-formats
  /etc/modprobe.d/uvcvideo.conf
    options uvcvideo quirks=128
v4l2capture
  apt-cache search v4l
  sudo apt install libv4l-0
v4l2 for python
  pip install pyv4l2
pip install pillow
modinfo uvcvideo

## Slide 13: MJpeg Streamer
Install
  sudo apt install libjpeg8-dev libv4l-dev
  tar zxvf mjpeg-streamer-master.tgz
Run server
  cd mjpg-streamer-master/mjpg-streamer-experimental/
  ./mjpg_streamer -i “./input_uvc.so -r 800x600” -o “output_http.so -w ./www”
View
  192.168.1.229:8080/stream.html

## Slide 14: Motion
Install and configure
  sudo apt install motion
  sudo vim /etc/motion/motion.conf
    daemon off -> on
    stream_localhost on -> off // Only stream to localhost
    webcontrol_local on -> off
  sudo vim /etc/default/motion
    start_motion_daemon=no -> yes
  sudo service motion start
View
  http://raspberrypi:8081 // stream
  http://raspberrypi:8080 // control

## Slide 15: MotionEyeOS - Basic
Ref
  https://github.com/ccrisan/motioneyeos/releases
Features
  The system listens on TCP port 80 (http), so can be accessed through browser
  motionEye: web frontend for the motion daemon
  motion: daemon, GPU not used
  three partitions: /boot, /, /data
Fast Network Camera
  streamEye: MJPEG streamer
  raspimjpeg.py
  no motion detection
WIFI Preconfiguration
  Create text file wpa_supplicant.conf
Launch
  login username: admin, no password
static_ip.conf
static_ip="192.168.0.3/24"
static_gw="192.168.0.1"
static_dns="8.8.8.8"
wpa_supplicant.conf
country=RC
update_config=1
ctrl_interface=/var/run/wpa_supplicant
network={
scan_ssid=1
ssid="crpa-meeting"
psk="zhongjingge"
}

## Slide 16: MotionEyeOS - Settings
Setting
  WIFI: /etc/init.d/S35wifi /data/etc/wpa_supplicant.conf -> /boot/wpa_supplicant.conf
  Ethernet: /etc/init.d/S40network /data/etc/static_ip.conf -> /boot/static_ip.conf
  motionEye: /programs/motioneye/settings.py /etc/init.d/S85motioneye /data/etc/motioneye.conf
  motion: /data/etc/motion.conf /data/etc/thread-x.conf
  Start Up: /data/etc/userinit.sh
  Modules: /data/etc/modules, /data/etc/modprobe.conf

## Slide 17: TODO
How to build or install python-v4l2capture?