## Slide 1: G-Code Notes
Last updated: 7/8/2022
Sparks Lu

## Slide 2: References
https://github.com/jminardi/mecode
https://marlinfw.org/docs/gcode/G000-G001.html
http://jherrm.com/gcode-viewer/
https://all3dp.com/2/gcode-viewer-3d-printer-simulator-best-tools/

## Slide 3: Overview
Intro
  G-code is the operational language for CNC machining.
  based on Cartesian coordinate system, right-hand rule
  standard language for most 3D printers
Actions
  Changing a pallet
  Rapid movement
  Controlled feed moves
  Controling feed movement
  Setting tool information

## Slide 4: Commands
Command | Meaning
G00 | rapid positioning, non-extrusion movement
G01 | moves the tool in a straight line to the designated coordinate, include extrusion
G02 | move clockwise in a circular or helical pattern, performing the appropriate machining process.
G03 | Same as G02, but in counter-clockwise
G04 | Dwell, pause the command queue, and wait for a period of time “G04 P<time(ms)>” “G04 S<time(sec)>”
G17 | X-Y plane selection
G18 | X-Z plane selection
G19 | Y-Z plane selection
G20 | Programming in inches
G21 | Programming in mm
G28 | Perform homing routine, “G28 X Y”
Command | Meaning
G90 | Use absolute positioning
G91 | Use relative positioning
G92 | Set current position, E axis (the filament position)
M5 | Spindle/Laser off
M104 | starts heating the extruder
M109 | wait until the desired temperature is reached
M140 | begins heating the bed
M190 | wait until the desired temperature is reached for the bed
M106 | Set fan speed
M201 | Set the max acceleration for one or more axes
M203 | Set the max feedrate
M204 | Set starting acceleration

## Slide 5: MeCode
MeCode
  https://github.com/jminardi/mecode
  pip install mecode
Function | 
set_home() | 
reset_home() | 
feed() | 
dwell() | 
home() | 
move() | 
abs_move() | 
arc() | 
abs_arc() | 
rect() | 
meander() | 
clip() | 
triangle_wave() | 
from mecode import G
with G(outfile='file.gcode') as g:
g.move(10)
g.view()

## Slide 6: SVG to GCode
pip install svg-to-gcode