## Slide 1: Media Notes
Sparks-Lu
Last updated: 8/13/2020

## Slide 2: References
https://helgeklein.com/blog/2017/12/browser-video-codecs-formats-hardware-acceleration/
https://www.fourcc.org/codecs.php
https://trac.ffmpeg.org/wiki/Encode/H.264
http://www.lighterra.com/papers/videoencodingh264/

## Slide 3: Video Container Format
MP4
  audio encoding: AAC, MP3
  video encoding: H.264 (AVC), H.265(HEVC)
  not royalty-free
WebM
  audio encoding: Ogg Vorbis
  video encoding: VP8, VP9
  royalty-free

## Slide 4: Video Standards
Name |  | Info
MPEG-1 | Used for VCD | 
MP3 | Part of MPEG-1 standard | 
MPEG-2 / H.262 | Used for DVD | 
MPEG-4 / H.264 | Used in Blu-ray | 
MPEG-H / H.265 / HEVC (High Efficiency Video Coding) | Support 4K and 8K resoluation | Doubles the data compression ratio compared to H.264

## Slide 5: Resolution Standard
Name | Resolution | Note
8K | 7680x4320 | 
4K | 4096x | 
UHD | 3840x2160 | Ultra High Definition
2K | 2048x | 
WUXGA | 1920x1200 | 
1080p | 1920x1080 | FHD (Full HD)
720p | 1280x720 | HD (High Definition)

## Slide 6: FourCC
Intro
  Short for “Four Character Code”
  An identifier for a video codec, compression format, color, or pixel format used in a media file.
Video Codecs by FourCC
  H264
  X264
  XVID

## Slide 7: FFMPEG 1/3
Install
  sudo add-apt-repository ppa:videolan/master-daily
  ffmpeg 3.3.3-2
Task | Commands | Note
Hide banner | ffmpeg -hide_banner | 
Log level | ffmpeg -loglevel error | 
pix format | ffmpeg -pix_fmts | 
Convert image sequences into video | ffmpeg -i %4d.png -r 20 output.mp4 | 
Get frames from image | ffmpeg -i input.mp4 output/frame%04d.jpg | 
Truncate video | ffmpeg -ss 10 -i input.mp3 -t 6 output.mp3 | 
Concat video files | ffmpeg -f concat -safe 0 -i mylist.txt -c copy output.mp4 | mylist.txt: file 'filename1'
Change video codec | ffmpeg -i in.mpg -c:v libx264 out.mp4 | 
List info | ffmpeg -codecs/-fomats/--decoders/--encoders/--filters | 

## Slide 8: FFMPEG 2/3
Task | Commands | Note
Remove audio from video | ffmpeg -i input.avi -vcodec copy -an output.avi | 
Merge audio and video | ffmpeg -i audio.mp3 -i input.mp4 output.mp4 | 
Change video size | ffmpeg -i input.avi -s 720x480 -c:a copy output.avi ffmpeg -i input.avi -filter:v scale=720:-1 -c:a copy output.avi | 
Crop video | ffmpeg -i input.mp4 -filter:v "crop=w:h:x:y" output.mp4 | 
Change fps | ffmpeg -i input.mp4 -r 30 output.mp4 | video lengh not changed, frames added or removed
Add logo to video (bottom-right) | ffmpeg -i vt.mp4 -i vhuantech-org.png -filter_complex "overlay=W-w-5:H-h-5" -codec:a copy TempleOfHeaven.mp4 | 
Speed up or slow down | ffmpeg -i input.mp4 -filter:v “setpts=0.6*PTS” output.mp4 | fps not changed, video length changed, frames added or removed

## Slide 9: FFMPEG 3/3
Task | Commands | Note
从MP4中提取声音 | ffmpeg -i input.mp4 -vn output.mp3 | 
Add subtitle | ffmpeg -i input.avi -vf subtitles=subtitle.srt output.avi ffmpeg -i input.avi -vf “ass=subtitle.ass” output.avi | 
Set h264 encoding params | ffmpeg -c:v libx264 -profile:v high/main/baseline -level:v 4.0 -crf 0~51 (constant rate factor, default 23, 0 lossless, 17/18 nearly lossless) // profile: video compression features the player must support // level: defines the peak bitrate the player can handle, along with the maximum resolution, and the maximum number of reference frames held in memory during playback | 
Padding | ffmpeg -i in.mp4 -vf “pad=width=800:height=600:x=10:y=75:color=black” out.mp4 | x/y: start placing point of the original frame
Web video | -movflags +faststart | 
Output to gif | ffmpeg -i input.mp4 -f gif output.gif | 
Reverse video | ffmpeg -i input.mov -filter:v 'reverse' -filter:a 'areverse' output.mov | 
Extract audio from video | ffmpeg -i input.mp4 -vn -ac 2 audio.wav | 

## Slide 10: Video Support in Safari
References
  https://developer.apple.com/library/archive/documentation/AppleApplications/Reference/SafariWebContent/CreatingVideoforSafarioniPhone/CreatingVideoforSafarioniPhone.html#//apple_ref/doc/uid/TP40006514-SW6
Supported
  H.264 Baseline Profile Level 3.0 video, up to 640 x 480 at 30 fps. Note that B frames are not supported in the Baseline profile
  MPEG-4 Part 2 video (Simple Profile)
  AAC-LC audio, up to 48 kHz
  .mov, .mp4, .m4v, and .3gp are supported
Server
  Must support byte-range requests
    curl --range 0-99 http://example.com/test.mov -o /dev/null

## Slide 11: Video Edit Software
References
  https://www.lifewire.com/best-free-video-editing-software-programs-4128924
OpenShot
  Windows, Mac, Linux
  Chinese version supported

## Slide 12: Subtitle
SRT format (.srt)
  Subrip Subtitle
  plain text
  time format: [hours]: [minutes]: [seconds], [milliseconds]
ASS format (.ass)
  Advanced SubStation Alpha subtitle
  ffmpeg -i input.srt output.ass
  ffmpeg -codecs | grep "^...S" // List supported subtitle codecs
[Section of subtitles number]
[Time the subtitle is displayed begins] –> [Time the subtitle is displayed ends]
[Subtitle]