## Slide 1: 3D Scanning
Sparks Lu
Last updated: 11-3-2020

## Slide 2: Type
Contact
Non-contact active
  laser
    time of flight
    triangulation
  structured light
Non-contact passive
  stereoscopic
  photometric

## Slide 3: Range Scanner
Theory
  Laser triangulation
Not good at
  shiny
  low surface albedo
  significant subsurface scattering

## Slide 4: Structured-light 3D Scanner
Theory
  consists of IR projector and IR sensor
Applications
  PrimeSense
  early version of Microsoft Kinect
  Occipital Structure Sensor
  Intel RealSense
  Face ID: projecting more than 30K infrared dots
Not good at
  reflective surface
  transparent or semi-transparent surface
  sub-surface scattering, such as skin, marble, wax, plants and human tissue
  concave surface

## Slide 5: Time of Flight Camera
Disadvantages
  background light
  interference
  multiple reflections
Application
  Microsoft Kinect 2nd generation

## Slide 6: Photogrammetry
Reference
  https://www.instructables.com/3D-Scan-Anything-Using-a-Camera-Photogrammetry-Wit/
Not suitable
  Moving object
  Having micro details, like leafy plants, hair and fur
  Reflective
  Transparent, translucent and untextured objects

## Slide 7: Products

## Slide 8: Reference
https://all3dp.com/1/best-3d-scanner-diy-handheld-app-software/

## Slide 9: Structured Light
Shining3D EinScan SE / SP
IIIDScan PrimeSense 3D Scanner
  Geometry camera: based on depth sensor 640x480
  Texture camera
XYZPrinting Handheld
  Based on Intel RealSense
Occipital Structure Sensor

## Slide 10: Laser Triangulation
NextEngine 3D Scanner HD
  max resolution: 0.1mm
FabScan Pi
Murobo Atlas
  system: Raspberry Pi
BQ Ciclop
  Arduino board
  Logitech webcam

## Slide 11: Photogrametry
3D Systems iSense

## Slide 12: TOF
Microsoft Kinect （2nd version)
  camera resolution: 1280x960