## Slide 1: Raspberry Setup
LOREM IPSUM DOLOR

## Slide 2: Change History
2024/3/23
  Updated for Raspberry PI 4b

## Slide 3: Intro
Versions
  Zero 2 W
  4b
  5
Pi 4B
Pi 5

## Slide 4: Raspberry Pi Zero 2W
Intro

## Slide 5: Rabian - Basic
OS
  Download Rasbian system image
    https://www.raspberrypi.org/downloads/raspbian/
    https://www.raspberrypi.com/software/
    Windows
      Remove all partitions
      Download Win32DiskImager
      Write Rasbian image to TF card
    Linux
      Etcher
      dd bs=4M if=2018-11-13-raspbian-stretch.img of=/dev/sdX conv=fsync
Config
  SSH
    Create empty “ssh” file in /boot to enable SSH service
Boot
  Username: pi
  Password: raspberry

## Slide 6: Network
References
  https://www.raspberrypi.com/documentation/computers/remote-access.html
VNC
  wayvnc as VNC server on Raspberry Pi
  Steps
    enable vnc server on Raspberry Pi
      Preferences > Raspberry Pi Configuration, Interfaces tab
      sudo raspi-config, “3 Interface Options”, “I2 VNC”
    ensure PC and RPI are connecting the same WiFi
    in pc, start TigerVNC viewer
    input VNC server (RPI) IP address
    in Options->”Input”, check “Show dot when no cursor”
    press Connect, input username and password
SSH
  IP address can be found using Angry IP Scanner
  ssh pi@raspberrypi.local
  rsync -avz -e ssh pi@192.168.1.10:camera/ camera/
  scp *.jpg <username>@<pi_ipaddr>:<path>
  scp -r folder/ <username>@<pi_ipaddr>:<path>
NFS
  Network File System (NFS) allows you to share a directory located on one networked computer with other computers or devices on the same network.
  client / server
Samba
  With Samba, you can share folders between Windows, macOS, and Linux machines.
Network boot
  You can set up a DHCP/TFTP server which will allow you to boot a Raspberry Pi 3 or 4 from the network.
Network
  /etc/network/interfaces
    iface usb0 inet static
    address 192.168.42.42
    netmask 255.255.255.0
    network 192.168.42.0
    broadcast 192.168.42.255
  wlan0
    auto wlan0
    allow-hotplug wlan0
    iface wlan0 inet dhcp
    wpa-ssid "P30"
    wpa-psk "vhuantech"

## Slide 7: Network 2
Commands
  ip addr show // show ip addresses
  arp -a // show ip addresses and host names
dhcp
USB Network
  Connect with Android phone using USB
  RPI: usb0 192.168.42.73
  phone: rndis0 192.168.42.129
  RPI recognize phone as network interface
WiFi Network
  nmtui
  raspi-config
  wpa_supplicant
    systemctl status wpa_supplicant
    journalctl -xe | grep wpa_supplicant
  sudo iwlist wlan0 scan | grep -A 9 "ESSID" # scan wifi hotspots
  iwgetid # get current wifi hotspot
  sudo iwconfig wlan0
  cat /proc/net/wireless
  nwcli
    nmcli connection show --active
    nmcli device wifi show-password
    nmcli connection down/up {SSID}
  sudo ifconfig wlan 0 down/up
  wpa_cli
    status
    list_networks
    scan
    scan_results
    select_network 1 # activate specified network and disable others
    set_network 1 ssid "MyHomeWiFi"
    set_network 1 psk "MyPassword"
    enable_network 1 # enable specified network
    reassociate
    save_config
    disconnect
    reconfigure
    quit
    echo -e "set_network 0 ssid \"P30\"\nset_network 0 psk \"vhuantech\"\nreassociate\nsave_config\nquit" | sudo wpa_cli -i wlan0

## Slide 8: Rasbian - Hardware Support
LCD
  Modify config.txt
WIFI
  /etc/wpa_supplicant/wpa_supplicant.conf
  wpa_supplicant.conf
  Static IP
    /etc/dhcpcd.conf
config.txt
max_usb_current=1
hdmi_group=2
hdmi_mode=87
hdmi_cvt 800 480 60 6 0 0 0
wpa_supplicant.conf
country=CN
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
network={
scan_ssid=1
ssid="yushidata"
psk="yushi@408"
key_mgmt=WPA-PSK
}
dhcpcd.conf
interface wlan0
static ip_address = 192.168.1.99
static routers = 192.168.1.1

## Slide 9: Camera
USB Camera
  IMX179
    FOV: 145, max: 3264x2448, 30fps
  OV2710
    FOV: 145, max: 1920x1080, 29fps
  OV5648
    max: 2592x1944, 30fps, FOV: 70, auto focus
  /dev/video0
  fswebcam <filename>
    sudo apt install fswebcam
    look for device /dev/video0
    -r <resolution>
    --fps <framerate>
  v4l2-ctl -V
Disable auto mount as USB storage
  .config/pcmanfm/LXDE-pi/pcmanfm.conf
    mount_on_startup=0, mount_removable=0, autorun=0
  reboot after change
sudo cat /sys/kernel/debug/usb/devices
v4l2-ctl
  v4l2-ctl --list-devices
    List devices
  v4l2-ctl --list-formats-ext
  v4l2-ctl -d /dev/video0 --list-formats
    list formats of video0
  v4l2-ctl -d /dev/video0 -l
    List controls
  v4l2-ctl -d /dev/video0 -D
    Show driver info
  v4l2-ctl -d /dev/video0 --all
    Show all info
ffmpeg
  ffmpeg -f v4l2 -video_size 1280x720 -i /dev/video0 -frames 1 out.jpg

## Slide 10: Bluetooth
References
  https://www.cnblogs.com/vamei/p/6753531.html
  https://www.oryoy.com/news/qing-song-shang-shou-shu-mei-pai-lan-ya-lian-jie-quan-gong-lve-python-ku-an-zhuang-xiang-jie.html
Service
  bluetoothd -v
  systemctl status bluetooth
  sudo systemctl start/stop bluetooth
  sudo systemctl enable bluetooth # configure to start on system boot
Command
  rfkill list // 查看系统中所有无线设备的状态，包括它们是否被软件或硬件屏蔽（blocked/unblocked）
  sudo rfkill unblock bluetooth
  bluetoothctl
    list, show, scan on, discoverable on
Service using Node.js
  curl -sL https://deb.nodesource.com/setup_16.x | sudo bash -
  sudo apt-get install nodejs
  npm install bleno
Dev
  sudo apt-get install pi-bluetooth bluez bluez-firmware blueman
  /etc/bluetooth/main.conf
  /var/lib/bluetooth/
    links

## Slide 11: Bluetooth Paring Issue
Solution 1
  https://developer.apple.com/forums/thread/678925
  1. Run "sudo vi /usr/lib/systemd/system/bluetooth.service".
  2. Add "-P battery" to the end of the ExecStart line. Save the file.
  3. Run "sudo systemctl daemon-reload" and "sudo systemctl restart bluetooth"
Solution 2
  Create setup_bt_agent.sh in /home/pi folder
  Create bt_agent.service
  Run “sudo cp bt_agent.service /etc/systemd/system/”
  Run “sudo systemctl enable bt_agent.service”
  Run “sudo systemctl start bt_agent.service”
#!/bin/bash
bluetoothctl <<EOF
agent off
agent NoInputNoOutput
default-agent
EOF
setup_bt_agent.sh
[Unit]
Description=Bluetooth Agent Setup
After=bluetooth.service
Requires=bluetooth.service
[Service]
ExecStart=/home/pi/setup_bt_agent.sh
Restart=no
[Install]
WantedBy=default.target
bt_agent.service

## Slide 12: Rasbian - Config
Apt source
  sudo nono /etc/apt/sources.list
  sudo nono /etc/apt/sources.list.d/raspi.list
Update S/W
  sudo apt update
  sudo apt upgrade
  sudo rpi-update
  sudo apt install vim
Auto login
  sudo raspi-config
  “3 Boot Options” -> “B1 Desktop/CLI” -> “B2 Console Autologin”
  “Localization Options” -> “Change TimeZone” -> “ShangHai”
Lauch python scripts when startup
  sudo crontab -e
  Add “@reboot sh /home/pi/bbt/launcher.sh >/home/pi/logs/cronlog 2>&1”
sources.list
deb http://mirrors.aliyun.com/raspbian/raspbian/ stretch main contrib non-free rpi
raspi.list
deb http://mirrors.aliyun.com/debian/ stretch main ui
sources.list
deb http://mirrors.aliyun.com/debian/ bookworm main contrib non-free non-free-firmware
deb-src http://mirrors.aliyun.com/debian/ bookworm main contrib non-free non-free-firmware
deb http://mirrors.aliyun.com/debian/ bookworm-updates main contrib non-free non-free-firmware
deb-src http://mirrors.aliyun.com/debian/ bookworm-updates main contrib non-free non-free-firmware
deb http://mirrors.aliyun.com/debian/ bookworm-backports main contrib non-free non-free-firmware
deb-src http://mirrors.aliyun.com/debian/ bookworm-backports main contrib non-free non-free-firmware
deb http://mirrors.aliyun.com/debian-security bookworm-security main contrib non-free non-free-firmware
deb-src http://mirrors.aliyun.com/debian-security bookworm-security main contrib non-free non-free-firmware

## Slide 13: Auto Start Program
Add script file to /etc/init.d/
  chmod 755
  test
    sudo /etc/init.d/yushi.sh start/stop
  enable when startup
    sudo update-rc.d yushi.sh defaults
  disable from startup
    sudo update-rc.d -f yushi.sh remove
#! /bin/sh
case "$1" in
start)
echo "noip is starting"
# Starting Programm
/usr/local/bin/noip2
;;
stop)
echo "noip is ending"
# Ending Programm
killall noip2
;;
*)
echo "Use: /etc/init.d/noip {start|stop}"
exit 1
;;
esac
exit 0

## Slide 14: Install Python Env
Pip/Virtualenv/Virtualenvwrapper
  sudo apt install python3-pip
  sudo pip3 install virtualenv virtualenvwrapper
  sudo apt install virtualenv virtualenvwrapper
  sudo rm -rf ~/.cache/pip
  Append lines to ~/.profile
  source ~/.profile
  mkvirtualenv py3 -p /usr/bin/python3
~/.profile
# virtualenv and virtualenvwrapper
export WORKON_HOME=$HOME/.virtualenvs
export VIRTUALENVWRAPPER_PYTHON=/usr/bin/python3
source /usr/share/virtualenvwrapper/virtualenvwrapper.sh

## Slide 15: Install Miniconda3
Miniconda3
  wget http://repo.continuum.io/miniconda/Miniconda3-latest-Linux-armv7l.sh
  md5sum Miniconda3-latest-Linux-armv7l.sh
  bash Miniconda3-latest-Linux-armv7l.sh
  source ~/.bashrc
  python --version (...Continuum...)
Virtualenv
  conda create --name py2 python=2
  source activate py2
  source deactivate
  conda install anaconda-client
Opencv
  conda install --channel https://conda.anaconda.org/poppy-project opencv3

## Slide 16: Berryconda
Berryconda
  wget https://github.com/jjhelmus/berryconda/releases/download/v2.0.0/Berryconda3-2.0.0-Linux-armv7l.sh
  bash Berryconda3-2.0.0-Linux-armv7l.sh
  source ~/.bashrc
  python --version (...Continuum...)
Virtualenv
  conda create --name py3 python=3
  source activate py3
  source deactivate
  conda install anaconda-client
Opencv
  conda install opencv3 scikit-learn

## Slide 17: Install OpenCV
Install numpy and dependencies
  pip install numpy
Download and build opencv
  sudo apt install python3-dev
  sudo apt install build-essential cmake pkg-config libjpeg-dev libtiff5-dev libjasper-dev libpng12-dev libavcodec-dev libavformat-dev libswscale-dev libv4l-dev libxvidcore-dev libx264-dev libatlas-base-dev gfortran
  wget -o opencv.zip https://github.com/opencv/opencv/archive/3.4.3.zip
  wget -o opencv_contrib.zip https://github.com/opencv/opencv_contrib/archive/3.4.3.zip
  unzip opencv.zip
  unzip opencv_contrib.zip
  cd opencv-3.4.3 && mkdir build && cd build
  cmake -D CMAKE_BUILD_TYPE=RELEASE -DCMAKE_INSTALL_PREFIX=/usr/local -D OPENCV_EXTRA_MODULES_PATH=~/opencv_contrib-3.4.3/modules -D ENABLE_NEON=ON -D ENABLE_VFPV3=ON -D BUILD_TESTS=OFF -D INSTALL_PYTHON_EXAMPLES=OFF -D BUILD_EXAMPLES=OFF
  Modify /etc/dphys-swapfile
    CONF_SWAPSIZE=1024
  sudo /etc/init.d/dphys-swapfile stop && sudo /etc/init.d/dphys-swapfile start
  make -j4 && sudo make install && sudo ldconfig
  cd /usr/local/lib/python3.5/site-packages && sudo mv cv2.cpython-35m-arm-linux-gnueabihf.so cv2.so
  cd ~/.virtualenvs/py3/lib/python3.5/site-packages/ && ln -s /usr/local/lib/python3.5/site-packages/cv2.so cv2.so
  Revert /etc/dphys-swapfile
    CONF_SWAPSIZE=100
  sudo /etc/init.d/dphys-swapfile stop && sudo /etc/init.d/dphys-swapfile start

## Slide 18: Clone SD Card
Backup
  sudo fdisk -l
  sudo dd bs=4M if=/dev/sdb of=~/hw/raspbian_11292018.img
    16G 13min
  sudo umount /dev/sdb1 /dev/sdb2
  fdisk -l raspbian.img
Restore or Clone
  Remove partitions if any
    sudo gparted
  sudo dd bs=4M if=~/hw/raspbian_11292018.img of=/dev/sdb
    5.0G 10min
    8.0G 20min

## Slide 19: V4L (Video4Linux) and Pillow
Commands
  v4l2-ctl
    v4l2-ctl --list-devices
    v4l2-ctl --list-formats-ext
    v4l2-ctl -d /dev/video0 --list-formats
  /etc/modprobe.d/uvcvideo.conf
    options uvcvideo quirks=128
v4l2capture
  apt-cache search v4l
  sudo apt install libv4l-0
v4l2 for python
  pip install pyv4l2
pip install pillow
modinfo uvcvideo

## Slide 20: MJpeg Streamer
Install
  sudo apt install libjpeg8-dev libv4l-dev
  tar zxvf mjpeg-streamer-master.tgz
Run server
  cd mjpg-streamer-master/mjpg-streamer-experimental/
  ./mjpg_streamer -i “./input_uvc.so -r 800x600” -o “output_http.so -w ./www”
View
  192.168.1.229:8080/stream.html

## Slide 21: Motion
Install and configure
  sudo apt install motion
  sudo vim /etc/motion/motion.conf
    daemon off -> on
    stream_localhost on -> off // Only stream to localhost
    webcontrol_local on -> off
  sudo vim /etc/default/motion
    start_motion_daemon=no -> yes
  sudo service motion start
View
  http://raspberrypi:8081 // stream
  http://raspberrypi:8080 // control

## Slide 22: MotionEyeOS - Basic
Ref
  https://github.com/ccrisan/motioneyeos/releases
Features
  The system listens on TCP port 80 (http), so can be accessed through browser
  motionEye: web frontend for the motion daemon
  motion: daemon, GPU not used
  three partitions: /boot, /, /data
Fast Network Camera
  streamEye: MJPEG streamer
  raspimjpeg.py
  no motion detection
WIFI Preconfiguration
  Create text file wpa_supplicant.conf
Launch
  login username: admin, no password
static_ip.conf
static_ip="192.168.0.3/24"
static_gw="192.168.0.1"
static_dns="8.8.8.8"
wpa_supplicant.conf
country=RC
update_config=1
ctrl_interface=/var/run/wpa_supplicant
network={
scan_ssid=1
ssid="crpa-meeting"
psk="zhongjingge"
}

## Slide 23: MotionEyeOS - Settings
Setting
  WIFI: /etc/init.d/S35wifi /data/etc/wpa_supplicant.conf -> /boot/wpa_supplicant.conf
  Ethernet: /etc/init.d/S40network /data/etc/static_ip.conf -> /boot/static_ip.conf
  motionEye: /programs/motioneye/settings.py /etc/init.d/S85motioneye /data/etc/motioneye.conf
  motion: /data/etc/motion.conf /data/etc/thread-x.conf
  Start Up: /data/etc/userinit.sh
  Modules: /data/etc/modules, /data/etc/modprobe.conf

## Slide 24: Clone SD Card
References
  https://www.raspberrypistarterkits.com/how-to/clone-raspberry-pi-sd-card-on-windows-linux-macos/
Steps
  Download Win32DiskImager and install
    https://sourceforge.net/projects/win32diskimager/files/latest/download
  Launch Win32 Disk Imager

## Slide 25: TODO
How to build or install python-v4l2capture?

## Slide 26: Photo Booth

## Slide 27: References
References
  https://www.instructables.com/Raspberry-Pi-photo-booth-controller/

## Slide 28: OS Image
Steps
  download Pi Imager from https://www.raspberrypi.com/software/
  run Pi Imager
  configure WIFI/ssh
After launch
  ping raspberrypi.local // get ip address

## Slide 29: Set Up for Photo Booth
Steps
  lsb_release -a
  update /etc/apt/sources.list and /etc/apt/sources.list.d/raspi.list
    将deb.debian.org替换为mirrors.aliyun.com
    将archive.raspberrypi.com替换为mirrors.aliyun.com
  sudo apt update
相机设置
  输出画质设置为S2（2400x1600）
打印机设置(USB)
  执行aiphotobooth/system/printer/setup.py
  在localhost:631中添加CP1500打印机
  在“Print Setting”中设置CP1500为系统缺省打印机
打印机设置(WiFi)
  连接WIFI热点
  树莓派打印机设置里找到CP1500
  修改CP1500的设置，加载Canon_SELPHY_CP1300.ppd
  在树莓派打印机设置界面打印测试页

## Slide 30: gphoto2
References
  http://gphoto.org/doc/manual/index.html
  http://gphoto.org/doc/remote/
  http://gphoto.org/doc/manual/using-gphoto2.html
Setup
  copy gphoto2-updater.sh, gphoto2.tgz and libgphoto2.tgz to device
  sudo ./gphoto-updater.sh
  copy prepare_usb_cam.sh to device
  sudo ./prepare_usb_cam.sh
  sudo reboot now
  gphoto2 --capture-image-and-download
Command | Note
gphoto2 --list-config | List config options
gphoto2 --list-ports | List ports
gphoto2 --auto-detect | Detect camera
gphoto2 --summary | Show camera summary info
gphoto2 -a | List all functions supported in camera
gphoto2 --list-files (-L) | List files
gphoto2 --get-all-files (-P) | Download all files
gphoto2--get-config {name} | Get one config value (liveviewsize, )
gphoto2--set-config {name}={value} | Set one config
gphoto2--set-config capturetarget=sdram | Store photo in RAM
gphoto2--set-config capturetarget=card | Store photo in SD card
gphoto2 --capture-preview | Store preview image as capture_preview.jpg
gphoto2--capture-image-and-download | Capture and download
gphoto2 --capture-movie --stdout ¦ ffmpeg -re -i pipe:0 -listen 1 -f mjpeg http://0.0.0.0:8080/feed.mjpg | preview
gphoto2 --set-config viewfinder=1 --set-config movierecordtarget=Card --wait-event=10s --set-config movierecordtarget=None --wait-event-and-download=2s | Record movie

## Slide 31: gphoto2 Liveview
Solution 1
  install v4l2loopback
    git clone https://github.com/umlaeute/v4l2loopback.git
    make && sudo make install
    sudo depmod -a
  gphoto2 autofocusdrive=1 --capture-movie --stdout | ffmpeg -i - -vcodec rawvideo -pix_fmt yuv420p -threads 0 -f v4l2 /dev/video0 -hide_banner -loglevel warning -nostats
Solution 2
  gphoto2 --get-config liveviewsize
  https://github.com/weebney/webcamize
    source webcamize
  open /dev/video0 for video
    ffmpeg -i /dev/video0 -ss 00:00:05 -vframes 1 output.jpg
    fswebcam output.jpg
Solution 3
  gphoto2 --capture-movie --stdout | ffmpeg -re -i pipe:0 -listen 1 -f mjpeg http://0.0.0.0:8080/feed.mjpg
    960x640
  open http://raspberrypi.local:8080/feed.mjpg stream in VLC media player

## Slide 32: Printer - USB连接
Set up printer
  Execute aiphotobooth/system/printer/setup.py
Add printer
  open “localhost:631” in browser
  add CP1500 printer
  in “Print Setting”, set CP1500 as system default printer

## Slide 33: Printer - WiFi连接
References
  https://www.voss.earth/2018/08/31/kurztipp-canon-selphy-wlan-drucker-cp910-oder-cp1300-unter-linux-cups-verwenden/
CP1500
  sudo apt install cups
  sudo usermod -a -G lpadmin pi
  sudo cupsctl --debug-logging --remote-admin --remote-any --share-printers
  sudo service cups restart
  open http://{ip_address}:631/
    e.g. http://192.168.55.69:631/
  open “Administration” page. Click “Add printer”, using Canon_SELPHY_CP1300.ppd
  input device username and password
  sudo lpstat -p
  sudo lpoptions
  lp HuGe.pdf // print
  sudo apt install imagemagick cups-client

## Slide 34: Electron
References
  https://azukidigital.com/blog/2019/electron-application-on-raspberry-pi/
Node
  copy node-v16.20.2-linux-arm64.tar.xz to device
  sudo tar zxvf node-v16.20.2-linux-arm64.tgz -C /usr/local/
  npm config set registry http://registry.npm.taobao.org/
  .npmrc
    ELECTRON_MIRROR="https://npmmirror.com/mirrors/electron/"
App
  copy app source folder to device
  cd app/src
  npm i
  npm run dev
printer
  https://github.com/tojocky/node-printer
  npm install printer --legacy-peer-deps
  sudo npm i -g node-gyp
  sudo apt install -y libcups2-dev
  npm i -D electron-rebuild
  cd node_modules/printer && node-gyp rebuild --arch=arm64 && cd ../..
  node_modules/.bin/electron-rebuild
Camera
  https://github.com/lwille/node-gphoto2
Create installer
  sudo npm i -g -S --verbose electron-installer-debian electron-packager
  electron-packager . aipb --platform=linux --arch=arm64 --out=./release-builds --overwrite
  node build-deb.js

## Slide 35: MJpeg Streamer
Install
  sudo apt-get install build-essential libjpeg-dev imagemagick libv4l-dev cmake git -y
  git clone https://github.com/jacksonliam/mjpg-streamer.git
  cd mjpg-streamer/mjpg-streamer-experimental
  make
  sudo make install
Usage
  /usr/local/bin/mjpg_streamer -i "input_uvc.so -f 15 -r 640x480" -o "output_http.so -w /usr/local/share/mjpg-streamer/www"
  http://raspberrypi.local:8080/

## Slide 36: EOS R100
CCAPI (Camera Control API)
  https://developercommunity.usa.canon.com/s/article/Introduction-to-Camera-Control-API-CCAPI
  RESTful API that will allow users to control compatible Canon cameras via HTTP commands. This allows user to control compatible cameras from almost any OS out there via WiFi.
  Introduced in 2022
EDSDK wrapper for Node.js
  https://github.com/dimensional-de/napi-canon-cameras
  https://github.com/intradeus/edsdk-wrapper-nodejs
  https://github.com/lwille/node-gphoto2

## Slide 37: Remote Desktop
references
  https://raspberrytips.com/remote-desktop-raspberry-p
steps
  sudo apt-get install xrdp
  sudo service xrdp start

## Slide 38: Printer - General
References
  https://www.baeldung.com/linux/cups
  https://www.linuxscrew.com/raspberry-pi-wireless-printer
  https://openprinting.github.io/cups/
  https://www.howtogeek.com/169679/how-to-add-a-printer-to-your-raspberry-pi-or-other-linux-computer/
  https://projects-raspberry.com/how-to-make-your-own-wireless-printer-with-a-raspberry-pi/
Set up
  sudo apt install cups cups-client printer-driver-all
  sudo usermod -a -G lpadmin {user}
  sudo cupsctl --remote-any
  sudo /etc/init.d/cups restart
  sudo lsusb # check for USB printer
  add printer
    open http://[the Pi's IP or hostname]:631 in browser to access CUPS portal (http://raspberrypi.local:631/)
    click “Administration” tab, click “Add Printer” button
  sudo lpstat -p // check printer
  sudo lp -d {printername} road.jpg

## Slide 39: Printer - Protocols
CUPS (Common Unix Printing Standard)
  uses IPP (Internet Printing Protocol) to manage local and network printers
  https://openprinting.github.io/cups/
  https://openprinting.github.io/cups/doc/admin.html
  provides the System V ("lp") and Berkeley ("lpr") command-line interfaces, a configurable web interface, a C API, and common print filters, drivers, and backends for printing
  http://localhost:631
  /etc/cups/cupsd.conf
IPP (Internet Printing Protocol)
  sudo ippfind
Commnad | Meaning
lpinfo -m | List available print drivers
lpinfo -v | List available printers
lpstat -p -d | List printer status
lpoptions -d {printer_name} | List printer options
lpoptions -d {printer_name} | Set default printer
lp {filename} -d {printer_name} -o media=A4 -o resolution=600dpi -o raw -o landscape -o fit-to-page -n {num-copies} | print file
cupsctl --debug-logging | 
cupsctl --no-debug-logging | 

## Slide 40: Printer - Gutenprint
References
  https://github.com/apple/cups/issues/6120
  https://github.com/OpenPrinting/ipp-usb/issues/73
  https://forums.linuxmint.com/viewtopic.php?t=391775
Gutenprint
  https://www.peachyphotos.com/blog/stories/building-modern-gutenprint/
  cups v2.4.2
  Gutenprint v5.3.4

## Slide 41: Printer - IPP-over-USB
References
  https://github.com/OpenPrinting/ipp-usb
  https://github.com/OpenPrinting/ipp-usb/issues/73
  https://wiki.debian.org/CUPSDriverlessPrinting#IPP-over-USB:_The_Basics
Intro
  A USB connected printer is seen as a network printer when IPP-over-USB is used.
Install
  sudo apt install snapd
  snap --version
  sudo snap install --edge ipp-usb
  restart Pi
  ipp-usb status
  ipp-usb check // potentially supported USB devices
  /var/log/ipp-usb/
  files
    /etc/ipp-usb/ipp-usb.conf
    /var/log/ipp-usb/

## Slide 42: Printer - IPP-over-USB 2
Build ipp-usb from source
  git clone https://github.com/OpenPrinting/ipp-usb.git
  sudo apt install golang
  export GO111MODULE=on
  export GOPROXY=https://goproxy.cn
  sudo apt-get install libusb-1.0-0-dev libusb-dev libudev-dev libavahi-client-dev
  sudo ldconfig
  make
  sudo make install
Commands
  systemctl list-units "ipp-usb*" | grep service
  systemctl status ipp-usb
  avahi-browse -rt _ipp._tcp
  driverless # get URI for printers
  lpstat -l -e
  ipp-usb status
  ipp-usb check

## Slide 43: Printer - Debug
References
  https://github.com/OpenPrinting/cups-filters/issues/492
  https://github.com/echiu64/Gutenprint
Debug
  sudo lpinfo -m # list printer driver modules
  edit /etc/cups/cups-files.conf
    change “FileDevice No” to “FileDevice Yes”
  dmesg # search for printer msg
  sudo ll /dev/bus/usb/{bus_id}/{device_id_on_bus} # get device ID
  sudo lpstat -t # no destination means no printer configured
  git clone https://github.com/echiu64/gutenprint.git
    autoreconf && ./configure && make && make install
  /var/log/cups/
  sudo lpoptions (default printer)
  sudo avahi-browse -rt _ipp._tcp
  sudo driverless

## Slide 44: Network
Intro
  With the release of Raspberry Pi OS Bookworm, networking on the Raspberry Pi was changed to use NetworkManager as the standard controller for networking, replacing the previous dhcpcd system.
Static IP
  Steps
    sudo nmcli -p connection show
    sudo nmcli c mod preconfigured ipv4.addresses 192.168.54.118 ipv4.method manuall
    sudo nmcli c down preconfigured && sudo nmcli c up preconfigured
WiFi Config
  sudo vi /etc/wpa_supplicant/wpa_supplicant.conf
  sudo raspi-config
    System Options->Wireless LAN->
  sudo nmtui
Network config
  sudo netstat -lptu
ufw
  sudo apt install ufw
  sudo ufw status
  sudo ufw enable

## Slide 45: USB Connection to PC
References
  https://www.makeuseof.com/how-to-connect-raspberry-pi-to-laptop-or-pc-usb/
  https://wiki.sipeed.com/hardware/en/maixsense/maixsense-a075v/install_drivers.html
Steps
  modify bootfs/config.txt
    append below line
      dtoverlay=dwc2 // enable the DWC2 (DesignWare Core) module, which manages the USB (Universal Serial Bus) functionality.
    comment out below line
      # otg_mode=1
  modify bootfs/cmdline.txt
    add below line immediately after “rootwait”
      modules-load=dwc2,g_ether
  download RNDIS driver from https://dl.sipeed.com/fileList/MaixSense/Drivers/Ethernet_RNDIS_drivers_20220808.zip
  in device manager, update driver for USB COM using downloaded driver
  check for “USB Ethernet/RNDIS Gadget in device manager
  ssh pi@raspberrypi.local

## Slide 46: Samba
Install
  sudo apt install samba
  sudo nano /etc/samba/smb.conf
    in [print$] block, change “read only = yes” to “read only = no”
  sudo systemctl restart smbd
Usage
  in Windows explorer, input “\\raspberrypi.local”