## Slide 1: Notes of Raspberry Pi
Sparks Lu
Last updated: 9/6/2018

## Slide 2: Build Kernel Image
Steps
  git clone https://github.com/RPI-Distro/pi-gen.git
  edit build.sh
  stages
    stage 0: bootstrap, stage 1: minimal, stage 2: lite, stage 3: desktop, stage 4: normal, stage 5: full
echo "IMG_NAME='raspios'" > config
touch ./stage3/SKIP ./stage4/SKIP ./stage5/SKIP
touch ./stage4/SKIP_IMAGES ./stage5/SKIP_IMAGES
sudo ./build.sh # or ./build-docker.sh

## Slide 3: Setup
Steps
  Download Raspbian Stretch Lite
    https://www.raspberrypi.org/downloads/raspbian/
  Download Etcher and write image image on microSD card
    Create empty "ssh" file in boot partition
    Create wpa_supplicant.conf
  Connect
    USB
    Ethernet
  Power on
    Check IP address of Pi
    ssh pi@ip
    password: raspberry
  WIFI
    disabled before WIFI country is set correctly
wpa_supplicant.conf
country=GB
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
network={
scan_ssid=1
ssid="Sparks"
psk="7001#mly"
proto=WPA
key_mgmt=WPA-PSK
}

## Slide 4: Config
raspi-config
  “Advanced Options” -> “Expand Filesystem”
  “Localisation Options” -> “Change Locale”
    Check “en_US.UTF8 UTF8”, “zh_CN.GBK GBK”, “zh_CN.UTF8 UTF8”
  “Localisation Options” -> “Change Wi-Fi Country”
    CN
  “Localisation Options” -> “Change Timezone”
    “Asia” -> “Shanghai”
WIFI
  sudo rfkill unblock wifi
  ip link set wlan0 up (or sudo ifconfig wlan0)
  Unplug ethernet
  Reboot
Set fixed IP address
  sudo nano /etc/dhcpcd.conf
Auto start after power on
  In /etc/rc.local, add “exec ...” before “exit 0”
dhcpcd.conf
interface wlan0
inform 192.168.31.188
static routers=192.168.31.1
static domain_name_servers=192.168.31.1
static domain_search=192.168.31.1

## Slide 5: Install Softwares
Apt Source
  modify /etc/apt/sources.list
    deb http://mirrors.tuna.tsinghua.edu.cn/raspbian/raspbian/ stretch main non-free contrib
    deb-src http://mirrors.tuna.tsinghua.edu.cn/raspbian/raspbian/ stretch main non-free contrib
  sudo apt update
  sudo apt dist-upgrade
Install softwares
  sudo apt install vim

## Slide 6: Install Python
Install Python
  sudo apt install python2.7-dev python3-dev
  wget https://bootstrap.pypa.io/get-pip.py
  sudo python get-pip.py
  sudo python3 get-pip.py
  sudo pip install virtualenv virtualenvwrapper
  sudo rm -rf ~/.cache/pip
  Edit ~/.profile as the one on the right
  source ~/.profile
  mkvirtualenv py3 -p python3
Install Python packages in virtualenv
  Modify pip.conf as the one on the right
  pip install numpy (slow)
~/.profile
export WORKON_HOME=$HOME/.virtualenvs
export VIRTUALENVWRAPPER_PYTHON=/usr/bin/python3
source /usr/local/bin/virtualenvwrapper.sh
/etc/pip.conf
[global]
index-url = https://pypi.tuna.tsinghua.edu.cn/simple

## Slide 7: Install OpenCV3
Install packages
  build-essential cmake pkg-config
  libjpeg-dev libtiff5-dev libjasper-dev libpng12-dev
  libavcodec-dev libavformat-dev libswscale-dev libv4l-dev libxvidcore-dev libx264-dev
  libgtk2.0-dev libgtk-3-dev
  libatlas-base-dev gfortran
  scp opencv-3.4.1.zip and opencv_contrib-3.4.1.zip to Pi
  Unzip opencv-3.4.1.zip and opencv_contrib-3.4.1.zip
  Build opencv
    cmake
      -D CMAKE_BUILD_TYPE=RELEASE -D CMAKE_INSTALL_PREFIX=/usr/local -D INSTALL_PYTHON_EXAMPLES=ON -D OPENCV_EXTRA_MODULES_PATH=~/opencv_contrib-3.4.1/modules -D BUILD_EXAMPLES=ON ..
    Modify /etc/dphys-swapfile CONF_SWAPSIZE to 1024
    sudo /etc/init.d/dphys-swapfile restart
    make -j4 && sudo make install && sudo ldconfig
    ln -s /usr/local/lib/python3.5/site-packages/cv2xxx.so ~/.virtualenv/py3.5/lib/python3.5/site-packages/cv2.so
    Revert /etc/dphys-swapfile CONF_SWAPSIZE to 1024
    sudo /etc/init.d/dphys-swapfile restart

## Slide 8: Setup Camera Module
Spec
  Sony IMX219 8MP sensor
  Max image resolution 2592*1944
  Supports 1080p30, 720p60 video
  CSI interface with Raspberry Pi
  Picamera python library
    pip install picamera
Connect Pi Camera with Raspberry Pi
  Ensure the connection is correct
Enable
  sudo raspi-config
    “Interfacing Options” -> “P1 Camera” -> Enable
  raspistill -o 1.jpg
  raspivid -o 1.h264 -t 10000
Refer
  https://picamera.readthedocs.io/
  https://elinux.org/RPi_USB_Webcams