## Slide 1: Canon Camera Notes
Last updated： 2024/8/27

## Slide 2: CCAPI

## Slide 3: Intro
Refrences
  https://developercommunity.usa.canon.com/s/article/CCAPI-Function-List
Intro
  RESTful API that will allow users to control compatible Canon cameras via HTTP commands. This allows user to control compatible cameras from almost any OS out there via WiFi.

## Slide 4: Function List - State and Settings
Function | URI | Note
Acquire support API table | http://[IPAddress]:[PortNumber]/ccapi/[Version] | 
Acquire camera's peculiar information | http://[IPAddress]:[PortNumber]/ccapi/[Version]/deviceinformation | 
Acquire accessible storage information in Camera | http://[IPAddress]:[PortNumber]/ccapi/[Version]/devicestatus/storage | 
Acquire battery information | http://[IPAddress]:[PortNumber]/ccapi/[Version]/devicestatus/battery | 
Acquire Temp Warning information | http://[IPAddress]:[Port]/ccapi/[Version]/devicestatus/temperature | 
Acquire lens information | http://[IPAddress]:[PortNumber]/ccapi/[Version]/devicestatus/lens | 
Copyright Information (Acquire,Update,Delete) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/copyright | 
Artist name (Acquire,Update,Delete) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/author | 
Owner's name (Acquire,Update,Delete) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/ownername | 
Nickname (Acquire,Update,Delete) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/nickname | 
Date and Time (Acquire,Update) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/datetime | 
Format a storage | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/cardformat | 
Silence settings (Acquire,Update) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/beep | 
Auto Display Off Settings (Acquire,Update) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/displayoff | 
Auto Power Off Settings (Acquire,Update) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/autopoweroff | 
Wi-Fi off | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/wificonnection | 
Setting Wi-Fi Connection | http://[IPAddress]:[PortNumber]/ccapi/[Version]/functions/wifisetting/[Set] | 

## Slide 5: Function List - Photography Control
Function | URI | Note
Acquire Storage URL | http://[IPAddress]:[PortNumber]/ccapi/[Version]/contents | 
Acquire URL of the directory under storage (DCIM) | http://[IPAddress]:[Port]/ccapi/[Version]/contents/sd | 
Remote Live View control | http://[IPAddress]:[Port]/ccapi/[Version]/shooting/liveview | 
Live View Flip | http://[IPAddress]:[Port]/ccapi/[Version]/shooting/liveview/flip | 
Capture still image | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/control/shutterbutton | 
Capture still image (Shutter Button control) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/control/shutterbutton/manual | 
Capture movie | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/control/recbutton | 
Zoom control | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/control/zoom | 
Focus drive | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/control/drivefocus | 
Perform AF (only) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/control/af | 

## Slide 6: Function List - Photography Setting
Function | URI | Note
Acquire current and range of all parameter | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings | 
Shooting mode (Auto/P/Tv/Av/M/Custom etc) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/shootingmodedial | 
AV | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/av | 
TV | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/tv | 
ISO | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/iso | 
Exposure (Exposure revision) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/exposure | 
White balance | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/wb | 
Color temperature | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/colortemperature | 
AF Operation in finder photography (Acquire) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/afoperation | 
AF Method of Live View (Acquire,Update) | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/afmethod | 
Quality of Still Image. | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/stillimagequality | 
Aspect ratio of still image | http://[IPAddress]:[PortNumber]/ccapi/[Version]/shooting/settings/stillimageaspectratio | 

## Slide 7: Live View
API
  POST /ccapi/ver100/shooting/liveview
    start live view
  GET /ccapi/ver100/shooting/liveview/flip
    get live view image